## Slide 1: Hat and Black Creek Clean Up Study
Nesha McRae
TMDL Coordinator, Valley Regional Office
January 30, 2023
Community Kick Off Meeting

## Slide 2: Goals for our meeting
Share what we know about Hat & Black Creek: Summarize monitoring data, discuss pollutants
Describe process we will use to identify and address pollution in the streams
Describe how you can get involved in this process
Answer your questions about this effort

## Slide 3: Hat and Black Creek Watersheds

## Slide 4: Why a study?
Aquatic life designated use
  All waters should support “the propagation and growth of a balanced, indigenous population of aquatic life”
What does this mean?
  Waters should be free of substances harmful to aquatic life
Monitor benthic macroinvertebrates (the bugs on the stream bottom) to determine if the standard is met
Photo: Jan Hamrsky: lifeinfreshwater.net

## Slide 5: Why should we care about bugs?
Consume algae and organic matter  nutrient cycling
Aquatic food chain
Our “canary in the coal mine”
Chemical monitoring = a snapshot in time
  Long lived
  Relatively immobile

## Slide 6: Determining a biological impairment
DEQ biological monitoring data (spring and fall)
VA Stream Condition Index is our barometer
  Diversity, pollution tolerance, feeding group
  Target score of ≥60

## Slide 7: Sensitive to pollution: Stoneflies
Photo: Jan Hamrsky: lifeinfreshwater.net

## Slide 8: Sensitive to pollution: Mayflies
Photo: Jan Hamrsky: lifeinfreshwater.net
Sensitive to pollution: Mayflies

## Slide 9: Caddisflies
Photo: Jan Hamrsky: lifeinfreshwater.net
Sensitive to pollution: Caddisflies

## Slide 10: Moderately Sensitive: Dragonflies
Photo: Jan Hamrsky: lifeinfreshwater.net

## Slide 11: Insensitive to Pollution: Blackflies
Photo: Jan Hamrsky: lifeinfreshwater.net

## Slide 12: Virginia Stream Condition Index
60
40
20
Photos: Jan Hamrsky: lifeinfreshwater.net

## Slide 13: DEQ Biological Monitoring Stations

## Slide 14: Black Creek Stream Condition Index Scores

## Slide 15: Hat Creek Stream Condition Index Scores

## Slide 16: Biological Impairments Determining the cause…
Benthic stressor analysis
  Evaluation of monitoring data
  Comparison with healthy reference watershed data and stressor thresholds
  Weight of evidence approach
  Identification of most likely stressor(s)
Photo: Jan Hamsky; www.lifeinfreshwater.net

## Slide 17: Candidate Stressors
Suspended solids
Deposited sediment
Dissolved oxygen
Phosphorus
Nitrogen
Ammonia
Total dissolved ions
Dissolved chloride
Dissolved sulfate
Dissolved sodium
Dissolved potassium
Dissolved metals
Temperature
Conductivity
pH
Organic matter
Sediment metals
Sediment toxics
Pesticides
Polycyclic Aromatic Hydrocarbons (PAHs)
Polychlorinated Biphenyls (PCBs)

## Slide 18: Weighing the Evidence: Sediment example
Intact streamside buffers
Eroding streambanks
Sediment deposits
Highly embedded

## Slide 19: Evidence of sediment as a stressor?
Biological monitoring data
  Filterers are predominant functional feeding groups, abundance of collections in Black Creek
  Abundance of net spinning caddisflies

## Slide 20: Net spinning caddisfly
Photo: Jan Hamrsky: lifeinfreshwater.net

## Slide 21: More evidence for sediment?
Stream bottom measurements
  More sand and fines in both Hat and Black Creeks

## Slide 22: More evidence for sediment?
Habitat measurements
  Both streams lack streamside vegetation (RIPVEG) and show evidence of sediment deposition (SEDIMENT)
  Bank erosion & embeddedness in Black Creek

## Slide 23: Phosphorus in Black Creek
High phosphorus concentrations
Low dissolved oxygen concentrations
Predominance of midge and black fly larvae (34%)

## Slide 24: What is a TMDL?
A Total Maximum Daily Load is the maximum amount of a pollutant that a waterbody can receive and still meet water quality standards.

## Slide 25: How do we develop a TMDL? What’s the magic number…
Identify sources of sediment and phosphorus
Model their path to the stream
Determine reductions needed from each source to restore aquatic life
Cropland:
10 tons/yr
Pasture: 12 tons/yr
Residential:
4 tons/yr
Forest:
1 ton/yr
Diagram: Adapted from the Center for TMDL and Watershed Studies at Virginia Tech
Urban:
8 tons/yr
Cropland:
30% reduction
Pasture: 40% reduction
Residential:
50% reduction
Forest:
0% reduction
TMDL
Sediment load = 19 tons/yr
Urban:
75% reduction
Impaired stream
Sediment load = 37 tons/yr
Point sources:
2 tons/yr
Point sources:
0% reduction

## Slide 26: More than just a number?
Primary objective is to address pollution in our waterways
TMDL study is the first step
Followed by an implementation plan
Implementation through partnerships with local organizations
Photo: Jan Hamsky; www.lifeinfreshwater.net

## Slide 27: How can you get involved? We need to hear from you!!!
Join the Advisory Committee
  Represents the local community
  Provides feedback on
    Stressors to the benthic community
    Land use
    Pollutant sources
    Key stakeholders and community meetings

## Slide 28: Join us for the first Stakeholder Meeting! Nelson Memorial Library March 1, 2023 2:00 p.m. – 4:00 p.m.
What’s Next?

## Slide 29: Questions & Comments
30-day public comment period (Jan. 25, 2023 – Feb. 24, 2023)
Send comments to:
Nesha McRae
PO Box 3000
Harrisonburg, VA 22801
Nesha.mcrae@deq.virginia.gov